## Slide 1: Two-way Partition Mar 10, 2022
TA: Siou-Sian Lin(林修賢)
Email: zu00895077@gmail.com
Advisor: Hung-Ming Cheng

## Slide 2: Outline
Problem Formulation
hMETIS introduction
Evaluation
Fm Partition Implementation

## Slide 3: Problem Formulation
Input
output
first line: # of nets and # of nodes
rest of lines: defined the nodes (named as 1 ~ n)
which the net is connected
The n-th line: group to the n-th node belongs
Notes: 可以用FM、KL、或其他你們知道的partitioning algorithm

## Slide 4: hMETIS introduction
An exe file which is dealing K-way partitioning
Usage: ./shmetis [input] [ # of groups ] [ balance factor ]
Ex: ./shmetis input.hgr 2 5
  And there will be a output file named input.hgr.part.2
Reference:
  hMETIS web
  Karypis, George, and Vipin Kumar. "Multilevel k-way hypergraph partitioning." VLSI design 11.3 (2000): 285-300.

## Slide 5: Evaluation
Your program:
  ./lab2 [input]
  Ex: ./lab2 input.hgr
  Output: output.txt
Verifier
  It will verify your output file and show the balance ratio
  Usage: ./verifier [input] [output]
  Ex: verifier input.hgr input.hgr.part.2

## Slide 6: Permission
Problem of permission
  Use chmod 755 [Executable binary]
  Ex:

## Slide 7
Fm Partition Implementation (optional)
Notes: 7

## Slide 8
What Is partition?
Target: partition the nodes to 2 sets and minimize the cuts number.
Notes: 8

## Slide 9
Common of FM & KL
Random initialization.
Choose best gain every time.
Locking mechanism.
Repeat R passes loop.
Notes: 9

## Slide 10
Difference of FM & KL
Moving way of node. (FM is more flexible)
Balance factor. (FM allow unbalanced partition)
Gain calculating. (FM can handle hypergraph)
Time complexity.
  KL : O(RN^3 )
  FM: O(RP ) (P is the total # of terminals)
Notes: 10

## Slide 11
What Is Terminal?
benchmark : ISPD98 Circuit-ibm18
W: Wires: 201920
N: Nodes: 210613
P: terminals: 819697
2 <= p <= N ,p is the terminals of every wire.
2N <= P <= WN ,P is the sum of the terminals in the circuit.
O(P)~=O(N) for normal circuit
Notes: 11

## Slide 12
FM Partition Flow
Random initialize
Construct gain list
Move node &
update gain list
All cumulative gain <0
End
NO
YES
+1
-1
+0
+2
-2
+p
-p
3
5
1
2
6
4
7
0
New Round

## Slide 13
+1
-1
+0
+2
-2
8
6
1
2
1
8
6
2
Move node
0
0

## Slide 14
+1
-1
+0
+2
-2
+1
-1
+0
+2
-2
8
6
1
2
1
0
8
6
2
0
1
6
2
8
1
8
2
Same color line is same line!
6
Move node

## Slide 15
1
3
4
5
0
8
7
6
2
9
update gain list

## Slide 16
+1
-1
+0
+2
-2
X
+p
-p
Calculate new gain
X
update gain list
update

## Slide 17
Experimental Results

## Slide 18: Thank you